## Slide 1: EE807 Software-defined Networked Computing
KyoungSoo Park
Department of Electrical Engineering
KAIST

## Slide 2: Class Overview
Recent hot topics in networking/networked systems research
  Software-defined networking (SDN)
  Network functions virtualization (NFV)
Activity: read and discuss research papers
  SIGCOMM, NSDI, CCR, NDSS, OSDI, SOSP, …
Goal: understand the concepts & develop and execute your own research ideas

## Slide 3: Administrativia
Lecturer: KyoungSoo Park
  Office: N1-813
  email: kyoungsoo@ee.kaist.ac.kr
  Homepage: http://www.ndsl.kaist.edu/~kyoungsoo/
No TAs for the course
  We may take turns if needed, but probably not

## Slide 4: Administrativia
Meeting time & Place
  M/W 10:30-11:45am
  Classroom: N1-114 (here)
Class homepage
  http://www.ndsl.kaist.edu/~kyoungsoo/ee807/
Piazza
  https://piazza.com/kaist.ac.kr/fall2014/ee807/home
  Paper review submission
  Online discussion

## Slide 5: Course Component: Paper Review
(1-)2 papers per class
  0.5 to 1 page for each review
Typical review format
  (1) summary of the paper
  (2) overall strength/weakness of the paper
  (3) in-depth review: most important
  Read “how to read a paper” by S. Keshav
  Linked to the syllabus page

## Slide 6: Course Component: Discussion Leading
Discussion leading
  Present a paper at each class (the first one)
  Defend the work as if it’s yours
  2 per semester, each graded by fellow students
  Important: introduce discussion points at the end
How to prepare your slides?
  Make your own slides: do not simply copy & paste original presenter’s slides
    You can borrow graphs and pictures with proper acknowledgement
  Read “how to give a good presentation”
    Linked to syllabus page (as well as other links)

## Slide 7: Course Component: Project
The most important part of the course
You develop/execute your own research idea
  By reading other ideas and how they execute
  In a group of one or two people (no more than two)
From idea inception to result presentation
  Motivation, design, implementation, evaluation
  Final paper: two-column, 10pt, 10+ pages
Don’t wait until the last minute
  Start thinking what would be intellectually challenging and useful, and fun!
  Discuss with me a rough idea before proposal

## Slide 8: Project Can be Literature Review
Pick a subject & read at least 10 papers (not discussed in class) around it
  Literature review should be an individual work
You review the subject
  Think of writing a survey paper
  10+ paper reviews + 1 final summary paper
  Proposal: what subject to review, why is it important, points to compare,…
  Presentation: overall review on the subject

## Slide 9: Grading
Discussion leading: 10%
  Graded by fellow students (by filling in a grading sheet)
Discussion participation: 10%
  Graded by professor (your grading sheet)
  Might take quizzes in case of lack of participation
Paper review: 30%
  1-2 papers per class, upload reviews to piazza before class starts (any late reviews are not counted)
  You have an option to skip two times (=1 week) throughout the semester (let me know when you skip)
Project proposal: 10%
  2-page write-up due 9pm on 10/18
Final presentation & paper: 30%

## Slide 10: Topics and Tentative Schedule
Introduction & preliminaries: 1 week
SDN technologies: 3 weeks
Verification, testing, debugging: 1.5 weeks
Project proposal (10/15)
Middleboxes and NFV: 5 weeks
Security issues: 1 week
Final presentation (12/10)

## Slide 11: Discussion Leading
Skim through the syllabus page
Let me know what paper to present ASAP
  Slots filled on a first-come-first-served basis
Before your presentation, meet me
  Set up an appointment by email
  At least 2-3 days before the presentation
  We’ll do practice talk with me with your slides
  I’ll give you feedback on your slides/presentation
  I’ll will check out the discussion points
Any questions?

## Slide 12: Computer Networks Review: (Some Important) Building Blocks

## Slide 13: Heat Map of the Entire Internet
From http://www.engadget.com/2014/08/29/internet-heat-map/

## Slide 14: Multiplexing
Cost-effective resource sharing
  Full-mesh network is not scalable: n(n-1) links
  Sharing links among multiple inputs/outputs
Statistical multiplexing
  Send from any available input sources
  No reservation needed for link use
    Utilize the pipe as much as possible
How to prevent starvation?
  Smaller pieces: packets

## Slide 15: Switching and Forwarding
Send data from a src port to a dest port
  Bridge, switch, router, etc.
Forwarding vs. routing?
  Forwarding: process of finding the right dest port by looking up the addr in the forwarding table
  Routing: process of building the forwarding table
Switching modes
  Circuit switching
  Packet switching
  Virtual circuit switching

## Slide 16: Circuit Switching
Exclusive dedication of a portion of the available bandwidth to carry traffic between src & dest
Bandwidth is allocated using:
  Frequency Division Multiplexing (FDM)
  Time Division Multiplexing (TDM)
Call requires three phases:
  Connection phase
    A circuit is set up between source and destination
  Transmission phase
    Traffic exchange takes place
  Termination phase
    The call is disconnected
Legacy telephone network, a typical example

## Slide 17: Circuit Switching
Advantages
  Guranateed bandwidth
  Simple abstraction: in-order delivery
  Fast forwarding: no need to look at header
  Low per-packet overhead
Disadvantages
  Wasted bandwidths
  Blocked connections when all resources are reserved
  Connection setup delay (RTT)
  Network state – per-connection state

## Slide 18: Packet Switching
No transmission capacity is dedicated along the routing path (efficient bandwidth utilization)
  No call setup needed before data transmission
  Data is transmitted in a sequence of packets
  Store and forward
Best-effort packet delivery
  Each packet is independent of each other
  Out-of-order delivery is possible
  No delivery guarantee
  No state preserved at the network

## Slide 19: Virtual Circuit Packet Switching
An initial phase is used to setup a fixed route
  Similar to circuit switching, except that a delay occurs at each node
  Call request and Call accept must both wait their turns for transmission
Upon path set-up, the virtual circuit appears to the user as a dedicated circuit
  The circuit is actually shared among multiple users
Destination address no longer required
  Only a virtual circuit number is needed
  Packets have shorter headers
  Faster forwarding
Packets follow the same routing path
  no order disruption
X.25, Frame Relay, ATM, MPLS, etc.

## Slide 20: Timing comparison

## Slide 21: Addressing
Providing suitable identifiers to nodes
  So you can direct data to a node (dest)
  So you know which node sent the data (src)
  …and how to send back to that node
Key concepts in addressing
  Number of unique addresses
  Flat vs. hierarchical structure
  Persistent vs. temporary identifiers
  Handling diminishing address space
  Spoofing of source addresses

## Slide 22: Comparing MAC and IP Addresses
 | MAC | IP
Assignment | Hard-coded in the adaptor | Configured or learned
Size | 48 bits | 32 bits (in v4)
Structure | Flat | Hierarchical
Portability | Constant over life of the adapter | Changes with time and location
Purpose | Delivery within a single network | Delivery across an inter-network
E.g., social security number vs. postal address

## Slide 23: Flow Control & Error Control
Flow control
  To prevent the receiver from overrunning
  Link layer vs. transport layer
    Stop-and-wait and sliding window algorithm
    TCP sliding window: receiver says “I can receive this much”
Error control
  Guards against loss or damage of data
  Mostly error detection and retransmission
    CRC-32 for Ethernet
    Internet checksum for IP header, UDP & TCP payload
  Should each layer independently implement its own?

## Slide 24: Congestion Control
Congestion control
  To prevent the network from overrunning
  Reduce the rate if you see a sign of congestion(= pkt loss)
    TCP : Additive Increase Multiplicative Decrease (AIMD)
  Explicit congestion notification (ECN)
    Router sets a bit in the TCP header
Issues with congestion control
  How to infer congestion?
  How to react to it?
  Who should enforce it?
  How to prevent malicious users?
  What are the goals?

## Slide 25: Performance Measures
Bandwidth vs. throughput
  Bandwidth: diameter of a pipe
  Throughput: measured bandwidth
Delay
  Propagation delay
  Transmission delay
  Queuing delay
Keep the pipe full
  Bandwidth-delay product
Transfer time = 1*RTT + data size/bandwidth
  How long it takes for the last byte to be ACK’ed
  Ignores queuing delay, errors and retransmission