## Slide 1: The Road to SDN: An Intellectual History of Programmable Networks
KyoungSoo Park
Department of Electrical Engineering
KAIST

## Slide 2: Paper Overview
How has the concept of SDN developed?
  20 years of compiled efforts
Summarizes the intellectual history of SDN
Three periods
  Active networking
  Control and data plane separation
  OpenFlow and network OSes

## Slide 3: Two SDN Characteristics
Why SDN?
Separating control plane from data plane
  Control plane: how to handle the traffic
  Data plane: forwards traffic based on the decisions that the control plane made
Consolidates the control plane
  A single software program controls “multiple” data-plane elements
  Direct control over the data-plane element’s state via well-defined API (e.g., OpenFlow)

## Slide 4: SDN Is a Hot Topic
Many interesting applications
  Dynamic access control, server load balancing, network virtualization, energy-efficient networking, VM migration, etc.
Many big Internet companies show interest
  Open Networking Foundation
  Open Daylight Initiative

## Slide 5: Active Networking
Between 1990 to 2000
  Tennenhouse and Wetherall
Make each networking node programmable
  Capsule mode: code to execute is carried in-band in data packets
  Programmable router/switch model: code to execute is established by out-of-band mechanisms
  First “clean-slate” approach to network architecture
Anathema to existing concepts
  “Network core should be simple and dumb”

## Slide 6: Active Networking
Technology pushes
  Reduction in the cost of computing
  Reasonable to put some computing in the core
  Java: platform portability, code execution safety
  Advancement in rapid code compilation, formal methods
  (Non technical) DARPA provide big funding

## Slide 7: Active Networking
Use pulls
  It’s too slow/hard to develop and deploy new services on the network (network ossification)
  Third-party interest in value-added, fine-grain control to dynamically meet the needs of particular applications/network conditions
  Researcher’s desire to experiment at scale
  Unified control over middleboxes (firewalls, proxies, transcoders)
Remarkably similar to those of SDN!

## Slide 8: Contributions of Active Networking
Programmability in the network to lower barrier to innovation
  Pioneered the notion of programmable networks
  AN focused more on data plane programmability
  Isolation of experimental traffic from normal traffic
Demux to software programs on packet headers
  NodeOS, Execution Environment (EE), Active Application (AA)
  Direct packets to EE: fast pattern matching on headers
Unified architecture for middlebox orchestration
  Early design documents hint at it
  But never fully realized

## Slide 9: Active Networking
Why not adopted?
  Lack of compelling problem
  Lack of clear path to deployment
No “Killer” application
  Caching, content distribution, application-specific QoS, information fusion,…, but not enough

## Slide 10: Separating Control and Data Planes
Circa. 2001 to 2007
Conventional routers/switches embody a tight integration between the control and data planes
  Debugging configuration problems is hard
  Predicting/controlling routing behavior is hard
Why not separate control and data planes?

## Slide 11: Separating Control and Data Planes
Technology push
  The Internet grows rapidly
  Packet forwarding implemented in hardware
  Separate from software-based control plane
  Servers have more memory and processing power than control-plane processors in a router
Open interface between the control/data planes
  ForCES (Forwarding and Control Element Separation)
  Netlink interface in Linux
Logically-centralize control of the network
  Routing Control Platform (RCP)

## Slide 12: Separating Control and Data Planes
Compared to Active Networking:
Focused on pressing problems in network management
  By and for network administrators
  Programmability in the control plane (rather than data plane)
  Network-wide visibility and control (rather than device-level configuration)

## Slide 13: Separating Control and Data Planes
Contributions:
Logically centralized control using an open interface to the data plane
  IETF (ForCES) defined an open, standard interface to install forwarding-table entries
  RCP used existing control plane protocol (BGP) to install forwarding-table entries
Distributed state management
  A logically centralized controller must be replicated to cope with controller failure, but replication introduces inconsistent state across replicas

## Slide 14: Separating Control and Data Planes
Criticism: no fate sharing
  Logically-centralized route control could fail independently from forwarding devices
  Centralized route control: each router has a purely local view of the “outcome” of the route selection
However, traditional distributed route selection also violates the principle
  Moving packet forwarding to hardware means that the control plane software could fail independently from the data plane

## Slide 15: OpenFlow and Network OSes
Success of experimental infrastructures
  PlanetLab
  Emulab
Global Environment for Network Innovation (GENI)
  Larry Peterson at SIGCOMM’05
Stanford created OpenFlow (‘07)
  Experimentation at a small scale: local campus network

## Slide 16: OpenFlow and Network OSes
OpenFlow faces trade-offs
  Fully programmable vs. pragmatic real-world deployment
  Enabling more functions than route controllers
  Building on commodity switches (limited flexibility)
OpenFlow API followed by NOX controller
  Each rule has a pattern (matches bits on header)
  A list of actions (drop, flood, forward, modify a header field, send the packet to controller)
  Counters and priority

## Slide 17: OpenFlow and Network OSes
Technology pushes
  Industry adoption of OpenFlow: Broadcom opened API to control certain forwarding behaviors
  Perfect storm for equipment vendors, chipset designers, network operators, networking researchers
  Switches already support necessary functions
  Start at a smaller scale and spread to a different venue (e.g., data center networks)

## Slide 18: Contributions of OpenFlow
Generalizing network devices and functions
  Can define forwarding behavior based on any set of 13 different packet header fields
  Same control on routers/switches/firewalls/NAT
The vision of a network operating system
  From NodeOS (AN) to network OS (OpenFlow)
Distributed state management techniques
  Multiple controllers for reliability, scalability, performance
  Work together to look like a single logically-centralized controller

## Slide 19: Myths of OpenFlow
“The first packet of every flow should go to the controller”?
  Ethane works this way, but others don’t need to
  OpenFlow has no assumption about the granularity of rules or whether controllers handle any traffic
  Some SDN applications only react to topology change
“SDN controllers must be centralized”?
  No! ONIX and ONOS are distributed
“OpenFlow == SDN”?
  OpenFlow is an instantiation of SDN principles

## Slide 20: SDN
Simply, it’s a tool that enables innovation in network control
  It does not solve any particular problem by itself
Can it be used to solve a pressing problem?
  That previous tools couldn’t have solved well
  Already showed some success in solving problems related to network virtualization

## Slide 21: Homework
Paper reviews: Ethane and 4D
  I will present Ethane and discuss Ethane/4D
Due on each class
Next time: 9/15 (Mon)
Have nice Chusuk!