## Slide 1: Ethane: Taking Control of the Enterprise
Presenter: KyoungSoo Park
Department of Electrical Engineering
KAIST

## Slide 2: Managing Enterprise Networks
Challenging to manage enterprise networks
  Often large networks
  Diverse applications
  Strict reliability and security
Current practice: error-prone & expensive
  62% of downtime due to human errors
  80% IT budgets on maintenance and operations

## Slide 3: Current Best Practices
Deploy middleboxes at network choke-points
Add functionality to networks
  User isolation: VLAN, ACL, filters, etc.
  Better connectivity management: instrument routing and spanning tree algorithms
Problem: hide complexity, but not reduce it!

## Slide 4: Goals
“Change the enterprise network architecture for better manageability”
Guiding Principles
Policy declared by high-level names
Policy should determine the paths
Strong binding between a packet and origin

## Slide 5: Policy by High-level Names
Users, hosts, groups access points as names
  Rather than IP or MAC addresses
  KyoungSoo talk to EE807 students via IM
  Marketing can use http via Web proxy
Why? addresses are dynamically changing
  Policy based on addresses could be unclear

## Slide 6: Policy Determines the Paths
Policy determines intermediate middleboxes
  “Guest should use a proxy to access Web”
  “Users on unpatched OS should go to IDS first before contacting other hosts”
Traffic receive more appropriate service
  “Real-time communication should be on lightly-loaded path”
  “Important traffic should be over redundant paths”
  “Private communication should be on trusted path”

## Slide 7: Binding of Packets and Origin
Addresses are dynamically managed
  Difficult to figure out who (user/host) sent packets
Tight binding of packets to their origin
  Fine-grain control of entire packets

## Slide 8: Ethane Design
Centralized Controller (smart)
  Enforces global network policy
  Decides the fate of a new flow (packets)
    ‘Allow or deny’ and ‘which route to take’
  Replicated for redundancy & performance
Ethane Switch (simple & dumb)
  Flow table and a secure channel to Controller
  Simply forward packets as directed by Controller
  Not every switch need to be Ethane switch

## Slide 9: High-Level Operation
Host authenticate hi, I’m host B, my password is …
Can I have an IP?
Send tcp SYN packet to host A port 2525
User Authentication “hi, I’m martin, my password is”
Domain Controller
Host A
Host Authentication “hi, I’m host A, my password is … can I have an IP address?”
Host B
User authentication hi, I’m Nick, my password is
?
Permission check
Route computation
Secure Binding State
ICQ → 2525/tcp
IP 1.2.3.4
switch3 port 4
Host A
IP 1.2.3.5
switch 1 port 2
HostB
Network Policy
“Nick can access Martin using ICQ”
Host A →
IP 1.2.3.4 →
Martin →
Host B →
IP 1.2.3.5 →
Nick →
Borrowed from Martin Casado’s slides

## Slide 10
Component Overview
Domain Controller
Switches
End-Hosts
Authenticates users/switches/end-hosts
Manages secure bindings
Contains network topology
Does permissions checking
Computes routes
Send topology information to the DC
Provide default connectivity to the DC
Enforce paths created by DC
Handle flow revocation
Specify access controls
Request access to services
Borrowed from Martin Casado’s slides

## Slide 11: Some Cool Consequences
Don’t have to maintain consistency of distributed access control lists
DC picks route for every flow
  Can interpose middleboxes on route
  Can isolate flow to be within physical boundaries
  Can isolate two sets of flows to traverse different switches
  Can load balance requests over different routes
DC determines how a switch processes a flow
  Different queue, priority classes, QoS, etc.
  Rate limit a flow
Amount of flow state is not a function of the network policy
Forwarding complexity is not a function of the network policy
Anti-mobility: can limit machines to particular physical ports
Can apply policy to network diagnostics
Borrowed from Martin Casado’s slides
Notes: Default connectivity  only to the DC

## Slide 12: Controller
Name registration
  Needs to know all entities in a network
  Any given global entry: LDAP or AD
Authentication
  Host: MAC address authentication, user: Kerberos
  Switch: SSL-based client/server-side certificates
Tracking all bindings
  Host to IP, IP to MAC address, User to Host
Permission check/access granting
Enforce resource limits
  Easy to enforce limits on flow rates, # of IP addresses, etc.
  Useful to defend against attacks (blocking after K trials)

## Slide 13: Controller Replication
Fault tolerance and scalability
  What happens if a controller fails?
  Scale the performance of request handling
Three models
  Cold standby
  Warm standby
  Fully-replicated

## Slide 14: Pol-Eth Policy Language
Domain-specific language for Ethane policy
  Conditions: action
  Actions: allow, deny, waypoints, outbound-only
Examples:
  “Phones” and “computers” don’t communicate
  “Laptops” are protected from inbound flows
Implementation
  Policy to C++ compiler

## Slide 15: Deployment
Prototype ran 4 months at Stanford
  300 registered machines
Switches and Controller
  19 switches of 3 different types
  A single PC-based Controller
Hosts: laptops, printers, VoIP phones, desktops, work stations, etc.

## Slide 16: Evaluation
Controller capacity
Impact of failures
  Controller failure
  Link failure
Flow table size

## Slide 17: How Many Controllers are Needed?
LBL trace (8,000 hosts): max 1,200 new flows /sec
Stanford trace (22,000 hosts): max 9,000 new flows /sec
Suggestion: a single controller should handle 20,000 hosts
Flow creation time as a function of load

## Slide 18: Impact of Controller Failure
How long does it take to reinstall flows?
  Measured completion time of 275 HTTP requests
  Intentionally crashed and restarted Controller
10% increase in completion time per failure
  Due to the model of cold-standby (learn routes again)
  Mitigated by warm-standby or fully-replicated Controllers

## Slide 19: Impact of Link Failures
Link failure: switch reports to Controller
  All flows on the link should be rerouted by Controller
Packet RTT during link failure (diamond topology)
~ 1+ sec of delay
Path reconverges
in under 40ms

## Slide 20: Flow Table Size
8K to 16K entries for university-sized network
  1MB (64B per entry)
  4MB (two-way hashing)
Typical Ethernet switch memory size
  1 million Ethernet addresses (6MB or larger)
  1 million IP addresses (4MB of TCAM)
  1-2 million of counters (8MB of SRAM)
  Several thousands of ACLs (TCAM)

## Slide 21: Ethane’s Shortcomings
Broadcast traffic
  ARP, OSPF neighbor discovery
Application layer routing
  A -> B, B ->C, but A !-> C: A->B->C
Knowing what the user is doing
  What if port 80 is used for bypassing firewalls?
Spoofing Ethernet addresses
  One port shared by multiple hosts?

## Slide 22: Ethane Summary
Centralized control by Ethane
  Separate the control and data plane
  Tightly manage Enterprise networks
Operations
  Centralized name bindings and authentication
  Dumb switch + Controller adopting new features
Deployment experience
  Easier to mange a network
  Easily identify network problems (errant machines, malicious flows)
  Hold users accountable for their traffic

## Slide 23: Discussion Points
Trade-offs of centralization
  What to gain, and what to lose?
Scalability beyond 10K machines
  How to distribute the load but centrally handle it?
Higher performance switch
  10G or higher, how many concurrent flows?
Apply it to cellular networks?
  Base stations or beyond?

## Slide 24: Goal of 4D Architecture
“Place control and management plane into a logically-centralized server”
Design principles
  Network-level objectives
  Network-wide view
  Direct control
Results in 4 planes

## Slide 25: 4D Architecture
Decision plane: all decisions in network control
  Reachability, access control, load balancing, security, etc.
Dissemination plane
  Connects routers/switches with decision elements
Discovery plane
  Discover physical components and create logical identifiers to represent them
Data plane
  Handles individual packets by forwarding table, packet filters, link weights, queue management params, etc.