## Slide 1: OpenFlow & NOX (& how the SDN era started) CCR 2008 Whitepapers
Nick McKeown & Natasha Gude et al.
Presented by: M. Asim Jamshed
Some slides have been derived from Nick McKeown’s talk in the Stanford Clean
Slate Program & Scott Shenker’s talk in the Open Networking Summit, 2011

## Slide 2: Intro: Need for a Programmable Switch
Alice wants to test a new network protocol
  Asks administrator to create network paths b/w set of machines spanning the entire campus network

## Slide 3: Intro: Need for a Programmable Switch
Control plane elements difficult to configure
  E.g. Network paths are fixed in L2/L3 boxes
  Flow tables in switches/routers vendor-specific
  Each L2/L3 path needs to be updated manually on each switch

## Slide 4: Approach I: Updating switch internally
Standard
Network
Processing
hw
sw
Experimenter writes experimental code on switch/router
User-
defined
Processing
*Figure taken from Nick McKoewn’s talk: “OpenFlow (Or: “Why can’t I innovate in my wiring closet?”)” (2008)
VENDOR’S
NIGHTMARE
Notes: Commercial vendor won’t open software and hardware development environment
  Complexity of support
  Market protection and barrier to entry

## Slide 5: Approach II: Open-S/W Platforms
Experimenter
uses Click
(or its equivalent)
FANOUT
COMPACT SOLUTION
Notes:   Hardware/software: Fanout too small (need >100 ports for wiring closet)

## Slide 6: OpenFlow Goals
Allow admins to program the control (forwarding) plane without exposing the IP rights of the vendors’
switches/routers
An open protocol that dynamically programs the flow tables in switches/routers

## Slide 7: OpenFlow Switching Approach
Controller
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow Protocol
(SSL)
hw
sw
OpenFlow Switch specification
*Figure taken from Nick McKoewn’s talk: “OpenFlow (Or: “Why can’t I innovate in my wiring closet?”)” (2008)
Commands/Packets
Notes: Amenable to high performance and low-cost implementations
Capable of supporting a broad range of research
Assured to isolate experimental traffic from production traffic
Consistent with vendors’ need for closed platforms

## Slide 8: Controller
Fine-grained management of the control plane
  Flows processed according to admin’s policies
Controller commands
  Forward packets to ports/controller
  Drop packets
  Rewrite headers
  Flexible header manipulation
    Arbitrary matching of first few bytes of payload
    Arbitrary rewriting of first few bytes of payload
Support load balancing b/w multiple controllers

## Slide 9: Secure Channel
SSL Connection, site-specific key
Controller discovery protocol
Encapsulate packets for controller
Send link/port state to controller

## Slide 10: Flow Table
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
+ mask
Packet + Byte counters
*Figure taken from Nick McKoewn’s talk: “OpenFlow (Or: “Why can’t I innovate in my wiring closet?”)” (2008)
Flow Table Entry

## Slide 11: End Targets
Amenable to
  High performance
  Low-cost implementations
Isolation of experimental from normal traffic
Vendor’s need for closed platforms retained
Notes: Amenable to high performance and low-cost implementations
Capable of supporting a broad range of research
Assured to isolate experimental traffic from production traffic
Consistent with vendors’ need for closed platforms

## Slide 12: The Bigger Question
Configuring each switch of the network for
  Path updates
  Access control
  VLAN tagging
  Traffic conditioning
  Traffic mirroring
Extremely cumbersome
    Manage control plane via programmable switches
      from a centralized node

## Slide 13: NOS Fundamentals
Present apps a centralized programming model
Manages the controller
Programs written as if the entire network is on a single machine
  High level abstractions
    IP and MAC address
    Hostnames and usernames
      Manage bindings between abstractions & low-level bindings
NOS network view  Entire network abstraction
An example of NOS  NOX (open source)

## Slide 14: SDN Hierarchy – The Big Picture
App
(Routing)
Simple Packet Forwarding (e.g. OpenFlow) H/W Switch
Simple Packet Forwarding (e.g. OpenFlow) H/W Switch
Simple Packet Forwarding (e.g. OpenFlow) H/W Switch
App
(CDN)
App
(AC)
Simple Packet Forwarding (e.g. OpenFlow) H/W Switch
Simple Packet Forwarding (e.g. OpenFlow) H/W Switch
Network Operating System (NOX)
1. Open interface to hardware
3. Well-defined open API
2. At least one good operating system
Extensible, possibly open-source
*Figure taken from Nick McKoewn’s FCC talk: “Software-Defined Networks” (2009)
Global Network View (DB)
ABSTRACT NETWORK MODEL
Notes: App = Control Program

## Slide 15: NOX Network Operations
Incoming new packet at switch
  Does flow entry for the corresponding flow exist?
  If yes:
    Perform the action
  If no:
    Forward it to the NOX controller
    Process the packet in the controller based on the policy written by the control program (app)
    Send NOX command to the switch to add new flow entry (optional)
Notes: - No command sent back for protocols such as DNS, DHCP etc.

## Slide 16: What more can NOX do?
Finer Admission Control
  “Guests can comm. using HTTP only via a web proxy”
VLANs
  “Create your own isolated network”
A non-IP network
  “Evaluate your own L3 protocol”
Simplistic scan detection
  How to detect scanning hosts
  Count # of unique L2 & L3 conn. initiation queries
    Concise (only 11 SLOC)

## Slide 17: Experiment at Packet Level
*Figure taken from “OpenFlow: Enabling Innovation in Campus Networks” (2008)
Deep Packet Inspection using a middlebox

## Slide 18: Experiment: Power Management

## Slide 19: Discussion Forum
Making the network more manageable
But also,
  Making the network more intelligent
Concept of “keeping the control plane simple” lost??
Notes: http://blog.silver-peak.com/an-insurmountable-problem-for-sdn

## Slide 20: Discussion Points
Data plane -> Control plane -> Data plane
  Latency issues?
Concept of security? (flow poisoning attacks)
Downside of using centralized management
  DDoS attack on the SDN controller
    100K DNS/DHCP requests per sec??
  Scalability
Difference between Ethane/NOX

## Slide 21: Appendix

## Slide 22: OpenFlow Switch Vendors
Alcatel-Lucent
Big Switch Networks
Brocade Communications
Arista Networks
Pica8
Cisco
Dell Force10
Extreme Networks
IBM
Juniper Networks
Hewlett-Packard
NEC
MikroTik
& many more…

## Slide 23: OpenFlow Type Switches
OpenFlow Switch Specification
  Current version 1.4 (2013)
Notes: Scalability? : Ethane controller can manage 10K new flows per second

## Slide 24: NOX Port Detection Example Code
scans = defaultdict(dict)
def check_for_scans(dp, inport, packet):
dstid = nox.resolve_host_dest(packet)
if dstid == None:
scans[packet.l2.srcaddr][packet.l2.dstaddr] = 1
if packet.l3 != None:
scans[packet.l2.srcaddr][packet.l3.dstaddr] = 1
if len(scans[packet.l2.srcaddr].keys()) > THRESHOLD:
print nox.resolve_user_source_name(packet)
print nox.resolve_host_source_name(packet)
# To be called on all packet-in events
nox.register_for_packet_in(check_for_scans)