## Slide 1: ClickOS and the Art of Network Function Virtualization
Joao Martins*, Mohamed Ahmed*, Costin Raiciu§, Roberto Bifulco*, Vladimir Olteanu§, Michio Honda*, Felipe Huici*
* NEC Labs Europe, Heidelberg, Germany
§ University Politehnica of Bucharest
Presenter : YoungGyoun Moon
EE807 - Software-defined Networked Computing
Some slides are brought from the authors’ presentation.

## Slide 2: The Idealized Network
Application
Transport
Network
Datalink
Physical
Datalink
Physical
Network
Datalink
Physical
Application
Transport
Network
Datalink
Physical

## Slide 3: A Middlebox World
carrier-grade NAT
load balancer
DPI
QoE monitor
ad insertion
BRAS
session border controller
transcoder
WAN accelerator
DDoS protection
firewall
IDS

## Slide 4: Typical Enterprise Networks
Internet
Notes: 기업 네트워크 (not ISP, data center)
IDS, Firewall / Proxy, Web content filtering, WAN Optimizer
덕지덕지, 관리하기도 어렵고 비용 증가 => 이걸 cloud 로 옮겨서 out sourcing 하면 어떨까?

## Slide 5: Hardware Middleboxes - Drawbacks
Expensive equipment/power costs
Difficult to add new features (vendor lock-in)
Difficult to manage
Cannot be scaled on demand (peak planning)
Notes: 그림을 추가하자!

## Slide 6: Shifting Middlebox Processing to Software
Can share the same hardware across multiple users/tenants
Reduced equipment/power costs through consolidation
Safe to try new features on a operational network/platform
But can it be built using commodity hardware while still achieving high performance?
ClickOS: tiny Xen-based virtual machine that runs Click
Notes: 좀 더 그림을 넣어서 SW 미들박스에 대한 인트로 보강하기

## Slide 7: Requirements for Software Middlebox
Fast Instantiation
Small footprint
Isolation
Flexibility
Performance
30 msec boot times
5MB when running
Provided by Xen
Provided by Click
10Gb/s line rate 45 μsec delay per packet
ClickOS
Notes: 1. Flash crowd  horizontal scaling  fast boot time
2. Hosting hundreds of middlebox VMs within a machine
3. Each middleboxes’ resources should be isolated + multiple MB from multiple vendors upon different operating systems
4. Should cope with wide range of middlebox functionalities
5. Datacenter or cellular ISP  requires high bandwidth, low delay

## Slide 8: What’s ClickOS ?
Work consisted of:
  Build system to create ClickOS images (5 MB in size)
  Emulating a Click control plane over MiniOS/Xen
  Reducing boot times (roughly 30 milliseconds)
  Optimizations to the data plane (10 Gb/s for almost all pkt sizes)
  Implementation of a wide range of middleboxes
apps
guest OS
paravirt
Click
mini OS
paravirt
domU
ClickOS
Notes: Under xen, normally vms are composed with this paravirtualization layer = small layer communicates with hypervisor to say program page tables, CPU timers, scheduling and so on. And on top of that we have your standard linux kernel or netBSD kernel with applications running on top.

## Slide 9: Programming Abstraction for MBox
Building MBox using Click
 We can use 300+ stock Click elements!
Notes: ClickOS uses Click as a programming abstraction for building up middleboxes.
Click enables modular packet processing, by using 300+ stock elemetnts. Mbox can be built up with minimal efforts.
Finding the best programming abstraction for middleboxes is an interesting research topic.. But not here 
 Running Click Efficiently: we could use Linux virtual machine for domain isolation.. But large footprint (128MB or more) and long boot time (5s) is the limitation.

## Slide 10: ClickOS
Click middlebox inside Linux VM
  (+) Can achieve domain isolation
  (-) Memory-hungry (128MB or more)
  (-) Large boot time (5 seconds to boot)
Click
guest OS
paravirt
domU
Notes: Linux VM (conventional VM)

## Slide 11: ClickOS
Why we use MiniOS?
  Single address space (= no kernel/user separation)
    Completely eliminates system call costs
  Runs a single application per VM
    Runs on single-core only (enough for 10Gbps packet processing)
  Cooperative scheduler
    Reduces context switch overhead
  Small footprint and minimal boot time
Click
guest OS
paravirt
Click
mini OS
paravirt
domU
ClickOS
Notes: In clickOS, what we do is we remove all of the conventional operating system, and we just use minimized for this purpose. And MiniOS is the basis for our ClickOS VMs.
MiniOS  Single-address space (no kernel/user space separation), No preemptive scheduler = Cooperative scheduler (application cooperates with kernel to run together), runs on single-core only. Just runs single application
In essence, it’s a vm just process packets.

## Slide 12: ClickOS Architecture
Console
Xen store = communication path (Dom0 - VM)
Allows the users to install Click configs in ClickOS VM
Set and retrieve state in elements (e.g. packet counter)
Notes: Two important paths
1. Network I/O path  Later
2. ClickOS control path
After the MiniOS boots, the control thread creates an install entry in the Xen store
 to allow users to install Click configurations in the ClickOS VM.

## Slide 13: ClickOS Boot Time
Tasks | Time spent
Issue and carry out the hypercall to create the VM | 5.2 ms
Build and boot VM image | 9.0 ms
Set up Xen store | 2.2 ms
Create the console | 4.4 ms
Attach VM to back-end switch | 1.4 ms
Install the Click configuration | 6.6 ms
Total | 28.8 ms
(optimized)
Re-designed the MiniOS toolchain for faster boot.
(added)
Provide a console through which Click configurations can be controlled
Notes: (Attach the VM to the back-end switch, connecting it to physical NICs)
1. MiniOS-based VMs by simply linking an application’s entry point so that it starts on VM boot.
2. a console through which configurations can be controlled

## Slide 14: Booting Large Number of ClickOS VMs
30 msec
220 msec
contention on the Xen store

## Slide 15: ClickOS Memory Footprint
 | Usage
Basic memory footprint of a ClickOS image | 5 MB
Netmap packet ring buffers (e.g. 2048-slot ring) | 8 MB
Middlebox application states (e.g. 1000 rules for IP router and firewall + 400 rules for IDS) | 137 KB
Total | < 14 MB
(optimized)
Includes 200+ supported Click elements and minimal set of libraries

## Slide 16: ClickOS
Work consisted of:
  Build system to create ClickOS images (5 MB in size)
  Emulating a Click control plane over MiniOS/Xen
  Reducing boot times (roughly 30 milliseconds)
  Optimizations to the data plane (10 Gb/s for almost all pkt sizes)
  Implementation of a wide range of middleboxes

## Slide 17: Performance Analysis
Packet size (bytes) | 10 Gbit/s rate
64 | 14.88 Mpps
128 | 8.4 Mpps
256 | 4.5 Mpps
512 | 2.3 Mpps
1024 | 1.2 Mpps
1500 | 810 Kpps
vif
Xen bus/store
Event channel
Xen ring API (data)
netback
netfront
OVS
native driver
Click
FromDevice
ToDevice
300 Kpps
350 Kpps
225 Kpps
(maximum sized packets)
Notes: Xen has a split-driver model, consists of netback and netfront drivers.
1. Netback driver runs in a driver domain, and manages virtual interface, which is connected to OVS.
2. Netfront driver runs at front-end in guest domain.
3. Communications between the two happen using shared memory and a common, ring-based API.
Finally, event channels are essentially Xen inter-VM interrupts, and are used to notify VMs about the availability of packets
Goal : to reach 10Gbps line rate

## Slide 18: Performance Analysis
Copying packets between guests greatly affects packet I/O (1)
Packet metadata allocations (2)
Backend switch is slow (3)
Mini netfront not as good as Linux
vif
Xen bus/store
Event channel
Xen ring API (data)
netback
netfront
OVS
native driver
Click
FromDevice
ToDevice
772 ns (1)
~ 600 ns (2)
~ 3.4 us (3)
Driver domain (Dom 0)
ClickOS domain
Notes: So let’s see what’s wrong here.
We did deeper analogies by looking at per-function call trace.

## Slide 19: Optimizing Network I/O
NF(netfront)-MiniOS-opt
  Reuse memory grants
  Now uses polling for Rx
NB-vale
  Introduce VALE as the backend switch
    Netmap-supported software switch for VMs (Luigi Rizzo, CoNEXT 2012)
  Increase I/O requests batch size
port
Xen bus/store
Event channel
netback
netfront
VALE
netmap driver
Click
FromDevice
ToDevice
Xen ring API (data)
Driver domain (Dom 0)
ClickOS domain
Notes:   Reuse memory grants
 to receive grants for packet buffers at initialization, and reuse them for future packet processing

## Slide 20: Optimizing Network I/O
Optimized Xen network I/O pipe
  netback : no longer involved with packet transfer
  netfront : use netmap API for better performance
    To map the packet buffers into its space directly
    More optimizations: asynchronous transmit, grant re-use
Optimized VALE
  Static MAC address-to-port mapping (instead of learning bridge)
Xen bus/store
Event channel
netback
netfront
VALE
netmap driver
Click
FromDevice
ToDevice
Directly mapped packet buffers
Driver domain (Dom 0)
ClickOS domain
Notes: Netback = only in charge of..
Setting up kernel threads that will handle packet transfer from VALE to netfront
(2) Allocating memory for Rx and Tx packet ring
Now we can remove unnecessary virtual interface and OS-specific structures (sk_buffs)
Netfront = map the ring packet buffers exposed by the ClickOS switch into its memory space

## Slide 21: ClickOS Prototype Overview
Click changes are minimal (~ 600 LoC)
  New toolstack for fast boot times
  Cross compile toolchain for MiniOS-based apps
netback changes comprise ~ 500 LoC
netfront changes comprise ~ 600 LoC
  We have implemented netfront driver for both MiniOS and Linux

## Slide 22: Evaluation

## Slide 23: Experiments
Delay compared with other systems
Switch performance for 1+ NICs
ClickOS/MiniOS performance
Chaining experiments
Scalability over multiple guests
Scalability over multiple NICs
Implementation and evaluation of middleboxes
Linux Performance

## Slide 24: ClickOS Base TX Performance
Intel Xeon E1220 4-core 3.2GHz (Sandy bridge)
16GB RAM, 1x Intel x520 10Gbps NIC
One CPU core assigned to VMs, the test to the Domain-0
Linux 3.6.10
ClickOS
Measurement Box
10Gb/s direct cable

## Slide 25: ClickOS Base TX Performance

## Slide 26: ClickOS Tx vs. Rx Performance
Notes: Rx bottleneck
extra queuing overheads at the netfront driver

## Slide 27: ClickOS (virtualized) Middlebox Performance
Intel Xeon E1220 4-core 3.2GHz (Sandy bridge)
16GB RAM, 1x Intel x520 10Gbps NIC
One CPU core assigned to VMs, 3 CPU cores for Domain-0
Linux 3.6.10
Host 1
Host 2
10Gb/s direct cable
10Gb/s direct cable
ClickOS

## Slide 28: ClickOS (virtualized) Middlebox Performance
Line rate for 512B pkts

## Slide 29: Chaining ClickOS VMs (back-to-back)
1 CPU core for running all the VMs
Notes: Ring size = 64
VM CPU bottleneck
Extra copy operation in the back-end switches (load on dom 0)

## Slide 30: Scaling out – 100VMs Aggregate Throughput
1 CPU core for running all the VMs (Tx only)

## Slide 31: Conclusions
Virtual machines can do flexible high speed networking
ClickOS: Tailor-made operating system for network processing
  Small is better: Low footprint is the key to heavy consolidation
  Memory footprint: 5MB
  Boot time: 30 ms
Future work:
  Massive consolidation of VMs (thousands)
  Improved Inter-VM communication for service chaining
  Reactive VMs (e.g., per-flow)

## Slide 32: Split/Merge (NSDI ‘13)
Virtualized middleboxes often require elasticity
  The ability to scale in/out to handle variations in workloads
Challenges
  Load distribution across VM replicas
  Middleboxes are mostly stateful
    How to keep consistency?

## Slide 33: Split/Merge
Virtual Network Interface!
Split
Replica 1 VM
Internal (e.g. cache)
VM
Coherent (e.g. packet counter)
Partitionable (Flow States)
Replica 2 Replica 3
VM VM
Unchanged
1
2
3
Coherency is
Interfaces!
maintained
Merge
Replica 1
Replica 2+3
VM
VM
1
2
Notes: Coherent  should be shared

## Slide 34: Discussion
Poor chaining performance
  NFV often requires service chain composed of multiple middleboxes
    Example  LB – NAT – WEB FW – INTERNAL LB – INTERNAL FW - ..
  What’s the solution?
    NetVM (NSDI ‘14) : zero-copy delivery for inter-VM communication

## Slide 35: Discussion
Design choice for Middlebox VMs
 | Linux VM | MiniOS
Memory footprint | 128 MB | 5 MB
Boot time | 5 s | 30 ms
Applications | Multiple apps can be run on a VM | Single app per VM
Performance | DPDK Open vSwitch | Optimized Xen I/O stack (netmap)

## Slide 36: Discussion
Virtualized middlebox
  Why we need virtualization?
    (+) isolation, easy migration, suitable for multi-tenant
    (-) performance!! / ClickOS (Rx+TX) : 3.7 Gbps for 64B pkt
  What’s the pros and cons for non-virtualized SW middlebox?

## Slide 37: Thank you for Listening! 

## Slide 38: Backup Slides

## Slide 39: Linux Guest Performance
Note that our Linux optimizations apply only to netmap-based applications

## Slide 40: Scaling out – Multiple NICs/VMs
Host 1
Host 2
6x 10Gb/s direct cable
6x 10Gb/s direct cable
ClickOS