## Slide 1: SIMPLE-fying Middlebox Policy Enforcement Using SDN
Zafar Ayyub Qazi, Cheng-Chun Tu, Luis Chiang
Vyas Sekar, Rui Miao, Minlan Yu
Presenter : ChoongHee Cho
Some slides are brought from the authors’ presentation.

## Slide 2: Current Network composition
Network component:
  - Nodes(e.g. switch or router)
  - Links
  - Middleboxes
: select L2 or L3 path
: connected road between the nodes
: L4-L7 function for network packet.
(e.g. critical performance, security, and
policy compliance capabilities, etc.)

## Slide 3: Middleboxes management is hard!
Critical for security, performance, compliance
But expensive, complex and difficult to manage
Survey across 57 network operators (J. Sherry et al. SIGCOMM 2012)
e.g., a network with ~2000 middleboxes required 500+ operators

## Slide 4: Middlebox with SDN
Benefits of SDN:
  logically centralized management
  providing the ability to programmatically configure forwarding rules.

## Slide 5
Can SDN simplify middlebox management?
Centralized Controller
“Flow” | FwdAction
… | …
“Flow” | FwdAction
… | …
OpenFlow
Proxy
IDS
Necessity + Opportunity:
Incorporate functions markets views as important
Scope: Enforce middlebox-specific steering policies
Firewall
IDS
Proxy
Web

## Slide 6
What makes this problem challenging?
Centralized Controller
“Flow” | FwdAction
… | …
“Flow” | FwdAction
… | …
OpenFlow
Proxy
IDS
1. Middleboxes introduce new dimensions beyond L2/L3 tasks.
Achieve this with unmodified middleboxes and existing SDN APIs
Firewall
IDS
Proxy
Web
2. Difficult to change middleboxes

## Slide 7: Our Work: SIMPLE
Firewall
IDS
Proxy
Web
Legacy
Middleboxes
OpenFlow
capable
Flow | Action
… | …
Flow | Action
… | …
Policy enforcement layer for
middlebox-specific “traffic steering”

## Slide 8: Outline
Motivation
Challenges
SIMPLE Design
Evaluation
Conclusions
8

## Slide 9: Challenges
Policy Composition
Resource Constraint
Dynamic Modifications
9

## Slide 10: Challenge: Policy Composition
S1
S2
Firewall
Proxy
IDS
Oops! Forward Pkt to IDS or Dst?
Dst
“Loops” Traditional flow rules may not suffice!
Firewall
IDS
Proxy
*
Policy Chain:

## Slide 11: Challenge: Resource Constraints
S1
S2
S4
S3
Proxy
Firewall
IDS1 = 50%
IDS2 = 50%
Space for
traffic split?
We should consider not only the middlebox resource constraints
but also switch TCAM space constraints
Firewall
IDS
Proxy
*
Policy Chain:
1) middlebox processing constraint
2) limited TCAM space in SDN switches
IDS
Resource constraints

## Slide 12
S1
Proxy
S2
User 1
User 2
Proxy may modify flows
Are forwarding rules at S2 correct?
Challenge: Dynamic Modifications
Firewall
User1: Proxy  Firewall
User2: Proxy

## Slide 13: New dimensions beyond Layer 2-3 tasks
1) Policy Composition  Potential loops
3) Dynamic Modifications  Correctness?
2) Resource Constraints  Switch + Middlebox
How can SIMPLE address these with unmodified middleboxes and
existing SDN APIs?

## Slide 14: Outline
Motivation + Context for the Work
Challenges
SIMPLE Design
Evaluation
Conclusion

## Slide 15: SIMPLE System Overview
Dynamics Handler
Legacy
Middleboxes
OpenFlow
capable
Rule Generator
Flow | Action
… | …
Flow | Action
… | …
Policy Chains
Firewall
IDS
Proxy
Web
Policy
Spec
Mbox, Switch
constraints
Topology, Traffic
Resource Manager
SDN Controller

## Slide 16: Composition  Tag Processing State
Firewall
IDS
Proxy
*
Policy Chain:
S1
S2
Firewall
Proxy
IDS
Dst
ORIGINAL
Post-Firewall
Post-IDS
Post-Proxy
Fwd to Dst
Insight: Distinguish different instances of the same packet

## Slide 17: Composition  Tag Processing State

## Slide 18: SIMPLE System Overview
Rule Generator
Resource Manager
Dynamics Handler
Legacy
Middleboxes
OpenFlow
capable
Flow | Action
… | …
Flow | Action
… | …
Topology, Traffic
Policy
Spec
Mbox, Switch
constraints
Firewall
IDS
Proxy
Web
Policy Chains
SDN Controller

## Slide 19: Resource Constraints Joint Optimization
Resource Manager
Topology & Traffic
Middlebox
Capacity + Footprints
Switch
TCAM
Policy
Spec
Optimal & Feasible
load balancing
Theoretically hard!
Not obvious if some configuration is feasible!

## Slide 20: Offline + Online Decomposition
Resource Manager
Network
Topology
Switch
TCAM
Policy
Spec
Traffic
Matrix
ILP-based
Offline Stage
Deals with Switch constraints
LP-based
Online Step
Deals with only load balancing
Mbox Capacity
+ Footprints

## Slide 21: Offline Stage: ILP based pruning
Set of all possible middlebox load distributions
Pruned Set
Balance the middlebox load
Feasible
Sufficient freedom

## Slide 22: SIMPLE System Overview
Rule Generator
Resource Manager
Dynamics Handler
Legacy
Middleboxes
OpenFlow
capable
Flow | Action
… | …
Flow | Action
… | …
Topology, Traffic
Policy
Spec
Mbox, Switch
constraints
Firewall
IDS
Proxy
Web
Policy Chains
SDN Controller

## Slide 23: Modifications  Infer flow correlations

## Slide 24: Modifications  Infer flow correlations
Three cases of flow correlations
  1) Not change the packet headers and flows
Directly map the incoming and outgoing flows
  2) Change packet header fields
Do an exact payload match between the incoming and outgoing packets
NAT
  3) Create new sessions or merge existing sessions
Calculate the (partial) similarities across flows

## Slide 25: Modifications  Infer flow correlations
Correlate
flows
Install rules
S1
Proxy
S2
User 1
User 2
Firewall
User1: Proxy  Firewall
User2: Proxy
Payload Similarity
With Rabin fingerprints

## Slide 26: SIMPLE Implementation
FW
IDS
Proxy
Web
Rule Generator
(Policy Composition)
Resource Manager
(Resource Constraint)
Modifications Handler
(Dynamic modifications)
OpenFlow 1.0
Flow | Tag/Tunnel | Action
… |  | …
Flow | Tag/Tunnel | Action
… |  | …
POX extensions
CPLEX

## Slide 27: Outline
Motivation + Context for the Work
Challenges
SIMPLE Design
Evaluation
Conclusion

## Slide 28: Evaluation and Methodology
What benefits SIMPLE offers? load balancing?
How scalable is the SIMPLE optimizer?
How close is the SIMPLE optimizer to the optimal?
How quickly it reacts to middlebox failure and traffic overload?
How accurate is the dynamic inference?
Methodology
  Small-scale real test bed experiments (Emulab)
  Evaluation over Mininet (with up to 60 nodes)
  Large-scale trace driven simulations (for convergence times)
  OpenvSwitch (v 1.7.1) as the SDN switch
  Custom Click modules to act as middleboxes

## Slide 29: Benefits: Load balancing
3-6X better load balancing and near optimal
Optimal

## Slide 30: Overhead: Reconfiguration Time
Around 125 ms to reconfigure, most time spent in pushing rules
33 node topology including 11 switches

## Slide 31: Other Key Results
LP solving takes 1s for a 252 node topology
  4-5 orders of magnitude faster than strawman optimization schemes
95 % accuracy in inferring flow correlations
  Duo to false policy rate and missed policy rate
Scalability of pruning(for a 250-node):
  1800s  110s

## Slide 32: Conclusions
Middleboxes: Necessity and opportunity for SDN
Goal: Simplify middlebox-specific policy enforcement
Challenges: Composition, resource constraints, modifications
SIMPLE: policy enforcement layer
  Does not modify middleboxes
  No changes to SDN APIs
  No visibility required into the internal of middleboxes
Scalable and offers 3-6X improvement in load balancing

## Slide 33: FlowTags
Commonalities and differences between SIMPLE and FlowTags
SIMPLE
FlowTags
Commonalities:
  Want to overcome the traffic handling problems of dynamic middlebox actions
  Uses SDN Architecture and Tags
Differences :
  FlowTags needs simple extensions of middlebox software
  FlowTags middleboxes have FlowTags tables and controller–middlebox interfaces
  FlowTags has verification, network diagnosis methods in the controller

## Slide 34: FlowTags architecture

## Slide 35: FlowTags example

## Slide 36: Evaluation

## Slide 37: Discussion
Possibility of rule that would not apply to switches at the same time – update timing issue.
Precomputing cost for switch, middlebox, and link failure scenarios.
  Pre-computing for all scenarios?
Countermeasure against DDOS attack(if all of packet is new)
Possibility of duplication use of ToS field
Multiple packets per flow case

## Slide 38: The End

## Slide 39: Apendix

## Slide 40: Decompose Optimization: Slow Offline + Fast Online Steps
Policy
Spec
Network
Topology
Enumerate
Physical
Sequences
Prune for
Feasible
Configs
Rule
Model
Offline Pruning
Traffic
Matrix
LP with PrunedSet
Mbox
Capacity
Online Load Balancing
PrunedSet
Notes: In order to efficiently solve the optimization problem, we decompose the problem into a slow offline stage and fast online step.
Offline stage that tackles the switch constraints
An online step runs a linear program that only deals with load balancing.
In the offline stage given a set of logical chains, we select a subset of the available physical sequences that will not violate the switch capacity constraints. The offline pruning stage only needs to run when the network topology, switches, middlebox placements, or the network policy changes. The online load balancing stage runs more frequently when traffic patterns change on shorter timescales.

## Slide 41: Enumerating Physical Sequences
S1
S6
S2
S5
FW1
FW2
10.1/16, HTTP  *
Firewall
IDS
 | Physical Sequence
FW1-IDS1-Proxy1 | S1 S2 FW1 S2 S4 S5 IDS1 S5 S4 S2 Proxy1 S2 S4 S5 S6
FW2-IDS1-Proxy1 | S1 S3 FW2 S3 S5 IDS1 S5 S4 S2 Proxy1 S2 S4 S5 S6
S3
Proxy
Policy Chains
Proxy1
IDS1
S4

## Slide 42: FlowTags‐enhanced controller

## Slide 43: Middlebox extension strategies to add FlowTags support
Notes: Module modification and Packet rewriting.
장점:
Input traffic consumption is One shot.
Suited for getting internal context in term of Tag generation.