## Slide 1: Serval: An End-Host Stack for Service-Centric Networking
Erik Nordstrom, David Shue, Prem Gopalan, Robert Kiefer, Matvey Arye, Steven Y. Ko, Jennifer Rexford, Michael J. Freedman
Princeton University
Presenter : YoungGyoun Moon
EE807 - Software-defined Networked Computing
Some slides are brought from the authors’ presentation.

## Slide 2: The Internet of the 1970s
Network designed only for accessing hosts
  Killer apps = telnet, ftp

## Slide 3: The Internet of the 2000s
Datacenter
Users require accessing “services”
  Agnostic of actual service location and host

## Slide 4: Requirements for Service Access
Finding a Service Location
  Map service name to location
Connecting to Service
  Load balance between pool of replicas
Maintaining Connectivity to Service
  Migrate between interfaces and networks

## Slide 5: Finding a Service Location
DNS binds service to location at client (early binding)
  Problem: caching and ignoring TTL / slow failover
DNS
Service Node 1
Service Node 2
Service Node 3
Load balancing
Fault tolerance
DNS update

## Slide 6: Connecting to Service
Datacenter LB maps a single IP to multiple servers
  Problem: must repeat this for every packet  fate sharing
  Problem: increases complexity and cost
Service Node
Load-balanced Web Service

## Slide 7: Maintaining Connectivity to Service
Problem: flows break when switching networks/interfaces
(a) Mobile client hosts
(b) VM Migration
Fixed Network
Cellular Network
Problem: requires flat addressing or tunneling
Datacenter
Host A
Host B

## Slide 8: Today’s Abstractions
Service is IP + port
  Exposes location
  Specifies app. protocol
  One service per IP
Flow is “five tuple”
  Binds flow to location
  Cannot migrate between interfaces or networks
connect (IP + port)
demux (IP + port)
forward (IP)
ex) KAIST web server
 143.248.5.130:80
Transport
Application
Network

## Slide 9: Serval Abstractions
Cleans the slate
  Network layer unmodified
Service Access Layer
  Connects to services
  Maintains connectivity
Transport
Application
Service Access
Network
forward (IP)

## Slide 10: Serval Abstractions
Service = ServiceID
  Group of processes with identical functionality
Flow = FlowID
  Invariant demux key
Location = IP address
  Location, interface (can change dynamically)
Transport
Application
Service Access
Network
connect (serviceID)
forward (IP)
demux ( )
serviceID
flowID

## Slide 11: A Clean Role Separation in the Stack
What you access (serviceID), over which flows (flowID), and at which service instance (IP address)
Transport
Application
Service Access
Network
connect (serviceID)
forward (IP)
demux ( )
serviceID
flowID
connect (IP + port)
demux (IP + port)
forward (IP)
TCP/IP
Serval

## Slide 12: A Service-Aware Network Stack
connect (sock, serviceID)
bind(sock, serviceID)
listen(sock)
Client side
Server side
Network stack must resolve service to instance
Network stack must advertise service

## Slide 13: Service Names (ServiceIDs)
ServiceIDs allocated in blocks
  Prefix ensures global uniqueness
  Enables prefix-based matching/aggregation
A ServiceID late binds to service instance
  ServiceID in first packet of connection
  Service-level routing and forwarding
Provider prefix
Provider-specific
Self-certifying

## Slide 14: Contributions
Naming abstractions
  Services, flows
  Clean role separation in the network stack
Software architecture for services (Serval)
  How network stack resolves/advertises service

## Slide 15: Serval End-host Architecture
Service-level control/data plane split

## Slide 16: Adding a Service Instance
Service Access Layer
ServiceID | Action | Rule state
X | DEMUX | Send to socket s
Application
Register Service X
s
Service Controller
bind(X)
listen()

## Slide 17: Removing a Service Instance
Service Access Layer
ServiceID | Action | Rule state
X | DEMUX | Send to socket s
ServiceID | Action | Rule state
Application
Unregister Service X
s
Service Controller
close()
Removed DEMUX Rule

## Slide 18: Data Plane: The Service Table
ServiceID | Action | Rule State
Prefix A | FORWARD | Send to address A1
Prefix B | FORWARD | Send to [A2, A3, A4]
Prefix C | DEMUX | Send to listening sock s
Prefix D | DELAY | Queue and notify service controller
Prefix E | DROP | -
default | FORWARD | Send to A5

## Slide 19: Service Router

## Slide 20: Client – Connecting to Service X

## Slide 21: Client – Connecting to Service X

## Slide 22: Service Router – Load Balancing

## Slide 23: Server – Providing Service X

## Slide 24: Server – Providing Service X

## Slide 25: Service Access with Serval

## Slide 26: Requirements for Service Access
Finding a Service Location
  Map service name to location
Connecting to Service
  Load balance between pool of replicas
Maintaining Connectivity to Service
  Migrate between interfaces and networks

## Slide 27: Migration of Flows

## Slide 28: Serval Prototype
End-host network stack (28,000 LOC)
  Linux kernel module
  BSD sockets with AF_SERVAL protocol familiy
    AF_INET sockets can be used simultaneously
Legacy middleboxes / NATs handled via encap.
Translator for incremental deployment
  Unmodified apps and end-hosts
Available at www.servalproject.org

## Slide 29: Base Performance Benchmark
TCP Throughput
Service Table Throughput
 | Mean (Mbit/s)
TCP/IP | 934.5
Serval | 933.8
Translator | 932.1
 | Mbit/s
IP forwarding | 987
Serval | 872

## Slide 30: Applications are Easy to Port

## Slide 31: Incremental Deployment

## Slide 32: Experimental Case Studies
Replicated Web Services
  Please refer to the paper
Back-End Distributed Storage
Use of Migration on Clients/Servers

## Slide 33: Back-end Distributed Storage
Dynamic partitioning mapping over 4 Memcached servers
  1 service router distributes queries over the four back-end servers
  Each has two 2.4 GHz AMD Opteron 2376 quad-core CPUs with GigE interface
Server 3 leaves
Server 2 leaves
Server 3 joins
Server 2 joins

## Slide 34: Use of Migration on Client
Wi-Fi
Cellular
Single Serval TCP connection that never breaks

## Slide 35: Use of Migration on Servers
Load balancing across NICs
Both flows use eth0
Flow 1 moved to eth 1

## Slide 36: Use of Migration on Servers
Migrating VMs across subnets
VM is assigned a new address
TCP stalls due to RSYN handshake

## Slide 37: Related Work
Locator/identifier separation
  HIP, i3, LISP, DOA, LNA
Data-oriented networking
  DONA, CCNx
Support for mobility and migration
  TCP Migrate, Mobile IP, DTP, ROAM
Multipath and multi-homing
  MPTCP, SCTP

## Slide 38: Conclusion
New naming abstractions
  Clean role separation in the stack
  Makes it easier to build and manage services
Software architecture for services
  Flexible service resolution and discovery
  Maintains robust connectivity
  Joint service and network management

## Slide 39: XIA : eXpressive Internet Architecture
Efficient support for evolvable internetworking
Define your own communication model
[Source: brought from the authors’ NSDI 12 slide]

## Slide 40: XIA : eXpressive Internet Architecture
[Source: brought from the authors’ NSDI 12 slide]

## Slide 41: Breaking Up the Transport Logjam
Incremental rollout of new or improved transports
Architecture
  Endpoint layer : intra-host addressing/routing via port num
  Flow Layer : manages end-to-end performance of flows
  Transport Layer : communication abstractions
    Ex) reliable byte stream / multi-stream (SCTP) / media frame (RTP)

## Slide 42: Breaking Up the Transport Logjam
Benefits
  Transport Implementation Flexibility
  Transport-Independent Middlebox Traversal
  Negotiation of Alternative Transports
RTSP
TCP
RTMP

## Slide 43: Discussion

## Slide 44: Discussion
Serval extends SDN to the edges
  SDN allows network-wide control on L2/L3
  Serval provides service-level control plane
What’s different with CCN?
  In line with CCN philosophy
  CCN has no notion of host even at its lowest level
  No existing CCN-based architecture clearly separates between service-level control/data plane

## Slide 45: Discussion
Deployment overhead
  Service controllers
    Additional cost to maintain globally unique provider ID
     (Professor) We can use hash of domain name.
    Additional cost to communicate between the controllers
  Service routers
    Higher computation, increased latency, installation cost
  Serval Translator
    Increased latency due to proxy, installation cost

## Slide 46: Discussion
FlowID security
  Serval RSYN process done without authentication
  Can Serval protect against connection hijacking?
Some utilities from DNS are not supported
  DNS caching is useful for many short-lived flows

## Slide 47: Thanks for listening 