## Slide 1: A Disruption-tolerant Transmission Protocol for Practical Mobile Data Offloading
Younghwan Go, YoungGyoun Moon, Giyoung Nam, and KyoungSoo Park
Department of Electrical Engineering
KAIST

## Slide 2: Mobile Devices as Post-PCs
Mobile devices are becoming similar to desktops in most areas of network communications
  VoIP, Gaming, File Sharing, M2M, Web, Video, etc.

## Slide 3: Mobile Data Explosion
Massive growth in mobile data communication
  Expected to surpass # of wired Internet users soon
18X

## Slide 4: Mobile Network Capacity Overload
3G, LTE unlikely to provide much bandwidth as the wired Internet  Capacity overload

## Slide 5: Existing Approaches
Increase physical capacity
  Reduce cell size
    Build more base stations (e.g., picocell, femtocell, cell tower)
    Costly
    Physical limitations due to signal interferences
  Multiplex the shared radio medium
    Cognitive radio
    Unable to cope with aggregate network demands

## Slide 6: Wi-Fi Offloading with DTN
Offload 3G traffic to cheap, high-bandwidth wired Internet through Wi-Fi before deadline expires
  Haggle [WONS’06], Wiffler [MobiSys’10], DTap [CoNEXT’10]
Server
3G Cell Tower
Client
Downloaded: 0%
Remaining: 6h
Downloaded: 50%
Remaining: 3h
Downloaded: 80%
Remaining: 1.5h
Internet
Wi-Fi AP
Time until Deadline
≤
3G Transfer Time
50%
4h
80%
2h
100%
0h

## Slide 7: Problem
Lack of system support for Wi-Fi offloading
  TCP binds host to physical network location (IP/port)
    Connection failure at IP/port changes  Restart
  Application-level resumption method
    Ad-hoc implementation for application separately
    Difficult to handle dynamically-generated content
Our Approach:
Transparently handle network disruptions in the transport layer regardless of host’s physical network location

## Slide 8: Our Solution
Disruption-tolerant Transmission Protocol (DTP)
  New transport layer protocol in mobile environments
  Reliable data transfer
  Transparently mask network failures to applications
  Provide illusion of continued connection regardless of physical network availability
Goal:
Transport layer support for practical mobile data offloading

## Slide 9: Related Works
Mobility for IP networks
  Mobile IP [JACS’95], i3 [SIGCOMM’02], HIP [RFC4423]
    Separate host identity with location by relaying to ID
    Require additional infrastructure support
  Migrate TCP option [MobiCom’00]
    Reuse connection after IP address change
    Cannot handle large disruption delays
Existing DTN protocols
  Bundle Protocol [RFC5050], LTP [RFC5325-5327]
    For challenged networks with high delays & packet losses
    Do not guarantee packet-level reliable data transfer
    Require pre-defined values for communication

## Slide 10: Contributions
No additional infrastructure support required
  Reliable data transfer on existing infrastructure
    Application developers do not need to handle disruption
TCP-mapped user-level UDP library
  Easy porting to existing applications
Efficient data transfer performance
  No retransmission from beginning after disruptions
  128.9% more throughput than TCP
  77.3% less power than always-connected 3G

## Slide 11: Wi-Fi Availability Measurements
Measurement in Seoul
  Visit 4 busy places
    Outdoor: Gangnam, Myongdong, Insadong
    Indoor: Coex
  4-day visit  27 hours of data
  Measurement method
    Client-to-server: 200 km
    Latency: ping at connection
    Bandwidth: Transmit large file

## Slide 12: Wi-Fi Availability Measurements
Finding:
Wi-Fi has larger bandwidth & smaller latency than 3G even in the busy places of a large city
Category | 3G | Wi-Fi
Availability | 100% | 45% (Bus/Subway) / 53% (Walk)
Latency | 130ms | 80ms
Bandwidth | 1 – 2 Mbps | 2.6 – 5 Mbps

## Slide 13: Wi-Fi Availability Analysis
Chart: Duration (seconds)
Chart: Duration (seconds)
50th Percentile:
6.6 min
50th Percentile:
7.8 min
90th Percentile:
1.1 h
90th Percentile:
5.7 h
Daily Trace [Yi. CoNEXT’10]
  97 iPhone users’ trace during 18 days
  Check network status (connection/inter-arrival time)

## Slide 14: Mobile Applications in Disruptions
7 popular applications
  Within the top 10 of each category
  100,000+ downloads
  Data transmission at network disconnections
Application | Category | Resumption method
Dropbox | Online storage | Not Supported
MapDroyd | Offline map access | Not Supported
Winamp | Podcast manager | Not Supported
Android Market | App. downloading | HTTP Range Request
Beyondpod | Podcast manager | HTTP Range Request
Google Listen | Podcast manager | HTTP Range Request
TubeMate | YouTube video | CGI Parameter Passing

## Slide 15: Contents
Introduction
Background
Design
Implementation
Evaluation
Conclusion

## Slide 16: TCP Not Suitable for DTN
TCP binds connection to host’s location (IP/port)
  Location change causes IP/port change
DTN causes frequent disruptions
  Constant switching between Wi-Fi & 3G
  TCP connection failure at every disruption
  Must restart data transfer from the beginning
How to provide seamless switching between disruptions?

## Slide 17: DTP: Delay-tolerant Transmission Protocol
Separate connection with host’s physical location
  Bind to a unique connection identifier
At disruption
  Maintain connection state in memory
  Illusion of continued, delayed connection
At reconnection
  Link to previous connection by connection identifier
  Resume communication from last position

## Slide 18: Flow ID
Unique ID bound to a connection
  Identify connection flow between two hosts
  Stay persistent even after location change
Advantages
  Application developers assume always-on connection
  Allow switching between Wi-Fi and 3G
    Seamless offloading for interactive or real-time data

## Slide 19: DTP Variables
Flow ID
  Identify a unique connection flow
Host ID
  Identify a unique host
Keep-Alive Duration
  Lifetime of a connection flow
CHG / RSP / AUTH
  Bit flags for authenticating ownership of flow ID

## Slide 20: DTP Communication
Connection Establishment
SYN:
Flow+ Host + Keep-Alive Duration (option)
Host A
Host B
SYN+ACK:
Host + Keep-Alive Duration (option)
ACK
Verify Flow ID

## Slide 21: DTP Communication
Data Transmission
Connection Setup
Host A
Host B
Data Transfer
Disruption…
Resume Data Transfer
Connection Teardown
Challenge:
Malicious user hijacks connection while “Host A” is in disruption
Solution:
Secret Key Exchange
&
Challenge-and-response

## Slide 22: DTP Communication
Secret Key Exchange
SYN:
Public Key:
Host A
Host B
SYN+ACK:
ACK
Generate secret key and encrypt it with Host A’s public key
Decrypt and retrieve secret key
Advantage:
Distribute decryption overhead to ‘n’ clients
Decryption:
SSL: By Server
DTP: By Client

## Slide 23: DTP Communication
Challenge-and-response
DATA or ACK:
Flow ID (new IP/port)
Host A
Host B
CHG +
RSP + -
Disruption…
Detect address change
AUTH

## Slide 24: DTP Communication
Connection Teardown
Host A
Data Transfer Done
Host B
Host A
Host B
Keep-Alive Duration
Expiration
Explicit
Connection Close
FIN
FIN+ACK
ACK
Data Transfer
Disruption…
Keep-Alive Duration Expired

## Slide 25: DTP API Library
UDP library to map TCP socket functions
  5,283 LOC
Exporting DTP library
  Wget (43,372 LOC)
  19 lines changed

## Slide 26: Implementation
Application thread
  Provide TCP socket-like functions to applications
Transport core thread
  Manage connection information
  Process sending/receiving of packets
Application Thread
Data
Connection
Socket
Transport Core Thread
Connection Table
Flow ID,
Host ID
Keep-Alive Duration, Secret Key, …
dtp_read()
dtp_write()
sendto()
sendmsg()
recvfrom()
Network

## Slide 27: Evaluation
Test
  Microbenchmark
    Throughput with no disruption (TCP vs. UDT vs. DTP)
  Performance at network disruption
    Throughput with disruption (TCP vs. BP vs. DTP)
  Power consumption
    Battery usage while transferring data with disruption
Device
  Client
    Laptop: i7-2620M CPU / 4GB RAM / Linux 2.6.40
    Phone: Nexus S / Android 2.6.35.7
  Server
    Desktop: i7-2600 CPU / 8GB RAM / Linux 2.6.38-12

## Slide 28: Microbenchmark
Laptop-to-server
DTP is comparable to TCP and UDT
Chart: Wired Transfer (1Gbps LAN)
| TCP | UDT | DTP
 | 942.268 | 912.146 | 945.85
Chart: Wireless Transfer (802.11n Wi-Fi AP)
| TCP | UDT | DTP
 | 44.07 | 43.59 | 43.82

## Slide 29: Performance at Network Disruptions
Video transfer size (number of disruption)
  77MB (0) / 154MB (1) / 308MB (2)
Connection/Disruption time = /7.8 minutes
Chart: Laptop-to-server
| 77 MB | 154 MB | 308 MB
TCP | 2.97 | 0.96 | 0.83
BP | 2.9 | 1.35 | 1.84
DTP | 2.95 | 1.42 | 1.9
Chart: Phone-to-server
| 77 MB | 154 MB | 308 MB
TCP | 2.97 | 0.96 | 0.84
DTP | 2.96 | 1.41 | 1.87
47.9%
128.9%
46.9%
122.6%

## Slide 30: Power Consumption
DTP-Wi-Fi (308MB file)
  vs. TCP-Wi-Fi
    1,655 sec less time
    58.3% less power
  vs. TCP-3G
    2,021 sec less time
    77.3% less power
Chart: Phone Power Consumption
| 0 | 99 | 299 | 449 | 601 | 749 | 898 | 1049 | 1198 | 1350 | 1501 | 1661 | 1811 | 1961 | 2110 | 2313 | 2462 | 2564 | 2711 | 2816 | 2962 | 3111 | 3264
TCP-3G | 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 89 | 88 | 87 | 86 | 85 | 84 | 83 | 82 | 81 | 80 | 79 | 78
TCP-Wi-Fi | 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 89 | 88 | 87 | 86 | 85 | 84 | 83 | 82 | 81 | 80 | 79 | 78
DTP-Wi-Fi | 100 | 99 | 98 | 97 | 96 | 95 | 94 | 93 | 92 | 91 | 90 | 89 | 88 | 87 | 86 | 85 | 84 | 83 | 82 | 81 | 80 | 79 | 78
Result:
Wi-Fi offloading with DTP requires less time and battery
to transmit data than always-connected 3G!

## Slide 31: Conclusion
Explosive growth of mobile data communication causes network capacity overload
Disruption-tolerant Transmission Protocol
  Identify connection with a unique flow ID
  Illusion of delayed transfer during disruptions
  Provide seamless switching between Wi-Fi & 3G
  High throughput / Low power consumption
Potential solution to reduce 3G network usage as well as the battery consumption

## Slide 32: Thank You! Any Questions?
http://www.ndsl.kaist.edu/

## Slide 33: Discussion
State Explosion Attack
  Create DTP connections with long keep-alive duration
    Minimal connection state
    Limit keep-alive duration value
    Reset keep-alive duration at attack detection
ISP-driven Offloading Servers
  Wi-Fi offloading for network resource utilization
    DTP cloud storage service
    Spread bandwidth consumption across time axis