## Slide 1: Software Packet Processing - The Click modular router - netmap: A novel framework for fast packet I/O
Presented by Shinae Woo
EE807 Software-defined Network Computing

## Slide 2: The Click modular router
EDDIE KOHLER, ROBERT MORRIS, BENJIE CHEN, JOHN JANNOTTI,
and M. FRANS KAASHOEK

## Slide 3: Router’s functionality
Routing + Forwarding
Do much more than routing and forwarding
Firewall
Packet filtering
Packet tunneling
Traffic prioritizing
Network address translation

## Slide 4: Routers in early 2000
Cisco ASR 1013
Cisco NCS 6008 Single Chassis System
Juniper E120 Broadband Services Router
HW routers
Specialized HW + proprietary SW
Monolithic, closed, static and inflexible
Difficult to add/delete functionality
SW routers
Commodity hardware + shipped with kernel
Hard to extend: Need to modify monolithic kernel code
x-kernel
scout
Streams
Netgraph
Q. How to design an extendable SW router platform?

## Slide 5: Requirements
No such solutions in early 2000 
1. Flexible and configurable router design
2. Extensible router design
3. Clearly defined interfaces
between router functionalities

## Slide 6: Click Modular Router
Divide
Conquer
Break down to individual router functionalities
Link individual functionalities
to complete a router design
Packet
classification
ARP query
Address lookup
Switching packets

## Slide 7: Click architecture
A directed graph with
Elements
  A single router function
Connections
  Possible packet path between two elements

## Slide 8: Elements
A single router function
Input and output ports
Configuration strings
  Per-element state, tuning behavior

## Slide 9: Connections
Possible paths for packet handoff
Building a routing configuration
1. Choose a collection of elements
2. Connect them into a directed graph

## Slide 10: Queue
Start with
packet arrival events
Start with
available packet transmission and scheduling events
Packet storage
NULL
1. Implicit queue in elements
2. Explicit queue outside elements
VS.
Queue: Unit for scheduling (single task or single thread)
Click’s choice

## Slide 11: Push and Pull Connections (1)
Queue
Destination
Source
receive packet p
ready to transmit
Push
Pull
enqueue packet p
dequeue packet p
Single scheduling unit
Single scheduling unit
push (p)
pull (p)
return
return

## Slide 12: Push and Pull Connections (11)
Single scheduling unit
Single scheduling unit
Push connection (▶■)
Pull connection (▷□)
Agnostic connection (double outline)
Becomes push or pull depending on peer
Either push or pull, not mixed

## Slide 13: Invalid connections between elements
1. Push output cannot connects to pull input
2. Push output cannot have more than one connection
3. Pull input cannot have more than one connection
4. Agnostic elements cannot
have mixed push/pull context

## Slide 14: Click implementation
Two versions
  Linux in-kernel driver: Good for production
  User-level driver: Good for profiling and debugging
Element
  C++ class
  20 virtual functions – need overwrite 6 or less
    push, pull, run_scheduled
Connection
  Virtual function calls between elements
Passing configuration file to the driver

## Slide 15: Simple languages for declarations and connections
Fully declarative
  Declaration
  Connection
  Not how to process packets
Shaper
ShapedQueue
Compound element

## Slide 16: IP Router
16 elements in push path
1 elements in pull path
Bring local information in packet e.g.,TTL
Bring annotated information with packets
  One element creates information
  Other element uses information e.g., Destination IP address, Paint (Marking packet with color)

## Slide 17: Extensibility
We can easily add additional functionality to IP router
Scheduling
Dropping Policy
Differentiated Services
Ethernet Switch
Covered in this talk

## Slide 18: Extensibility (1) Scheduling
Stochastic Fairness Queueing (SFQ)
  Providing isolation between competing flows
  Distributing packets into multiple queues
Virtual queue

## Slide 19: Extensibility (2) Dropping policy
Weighted Random Early Detection (RED)
  Red: Dropping packets with network congestion
RED element needs to know ‘nearest downstream queue’
  S1. Manual configuration to give the information
  S2. Flow-based router context
What is your queue length?
My queue length is 10

## Slide 20: Flow-based router context
Answers for
If I were to emit a packet on my second output,
  Where might it go?
  Which queues might it encounter?
 Using a simple data-flow algorithm on configuration graph
RED: Where is my nearest down stream queue?

## Slide 21: Evaluation environment
Source
Destination
Click IP Router
100 Mbit/s
700 MHz Intel Pentium Ⅲ
733 MHz Intel Pentium Ⅲ
200 MHz Intel Pentium Pro
UDP packets
147,900 64B PPS
100 Mbit/s
Make a bottlneck

## Slide 22: Simple forwarding rate
Click keeps the baseline performance of Linux
Peak: 360,000 PPS
Loss-free: 333,000 PPS
Linux routing table algorithm
is slower than Click’s
Receive live rock
Click’s polling driver avoiding interrupts and efficient I/O

## Slide 23: Forwarding rate with richer functionality
Comparison with real network
  Not involve: fragmentation, IP options, ICMP error
  Smaller number of ARP entries
Click’s performance drops only gradually

## Slide 24: Overhead of modularity
Overhead of passing packets between elements
  Single virtual function call: 70 ns
  16 elements in IP router: 70 ns * 16 = 1 us / packet
Combine multiple elements into one
  16 elements  8 elements
  Number of virtual function calls will decrease
Push path latency decreases
  1.57 us  1.03 us

## Slide 25: Overhead of modularity
Unnecessarily general element code
Implemented more generality than necessary
Classifier
  Required for IP router: ARP, IP packets
  Implemented: a small data structure for finding which packet data to examine
  Special classifier
    24% smaller CPU cycles than general classifier
    But only 4% less than total cost

## Slide 26: Conclusion
Click Modular Router
An open, extensible, and configurable router framework
Building a complex IP router by connecting small, modular elements
Modularity does not harm the performance of the base Linux system
Easily adding extended functionality
http://www.read.cs.ucla.edu/click/

## Slide 27: netmap: a novel framework for fast packet processing
Luigi Rizzo

## Slide 28: netmap: a novel framework for fast packet processing
Possible number of packets @ a 10G link
  14.88 Mpps (64B packets)
Packet processing overhead in commodity OS
  Per-packet dynamic memory allocation
  System call overhead
  Memory copies
netmap
  60-65 cycles/packet (67 ns)
sendto() execution path and time in FreeBSD
system call
1us / packet
1.05 Mbps

## Slide 29: netmap architecture
Netmap’s approaches
  Per-packet dynamic memory allocation  Preallocated resources
  System call overhead  Large batching
  Memory copies  Shared buffer between kernel and userspace

## Slide 30: Evaluation
Test equipment
i7-870 4 core @ 2.93MHz
Intel 82599 10G NIC
64B packet Tx
netmap: 60-65 cycles/packet
Line rate
8x

## Slide 31: Discussion

## Slide 32: Click implicit dependency from annotation
Annotation makes implicit dependency between elements
  There are 16 annotation types in the paper (+ custom types now)
  How to resolve those dependency?
  There are no consideration on the configuration step
Paint
CheckPaint
Set paint annotation
Use paint annotation

## Slide 33: Click Extend to support L4/Stateful functionality
How to support TCP functionality
  Can be built as a single element
  Cannot support modularity on L4 layer
How to support IP defragmentation
  It has to reserve packets until the other parts of packets arrived
  Click elements requires to store packets
TCP

## Slide 34: Click Tradeoff between modularity vs efficiency
There are fundamental tradeoff between modularity and efficiency
VS.
How can we get both benefit?
  Give a configuration in a modular way
  Optimize binary to integrated functionality
IPPush

## Slide 35: netmap Comparison between other apporoaches
There are many similar work in this area
  PSIO, PF_RING, DPDK
Similar approaches to solve same challenges
Benefit from netmap compared with other approaches
  Integrated with FreeBSD
  Not depend on specific hardware